I bought mine (a .177cal) about halfway thru the initial buying craze that passed thru here. I still can't stop playing with it!

I didn't do a tear-down with a  interior hone, buff, polish, and proper lube, but instead I did a simple exterior clean-up of all I could, added a copper shim under the cocking arm's pivot, lubed it all well,  installed a Brass trigger shoe, and a trigger stop bolt. I am sure the simple mods that I did, could be accentuated with a proper teardown and re-build, but they sure made a world of difference on my rifle! I just broke mine in thru shooting it, and it has been a constant, all stock, and out of the box, GOOD performer.

The trigger pull is the worst complaint from most F/D owners, and can be dealt with as Russ has done. A  good "Tuner", or even a semi-competent owner can refine the rifles interior parts to various stages of improvement and the rifle will benefit from such work. *Unless you are familiar with trigger work as Russ is, be careful removing metal there!

Mine is now mounted with a fixed 4 power BSA scope, and between 10 and 30 m,  nary a soda can escapes! The velocity on my rifle is 630 fps with 7.9 gr pellets. These days it is barely considered hunting speed, but back when I learned to use a springer, that MV would (and will still) take a lot of pests with properly placed hits!

These rifles are plenty accurate enough for many hours of fun shooting, be it targets, plinking, or light hunting.  Construction is all wood and steel, and though the metalwork is crudely finished in comparison to European rifles. You still won't have an ounce of shame being seen with one, and with the ruggedness of the rifle, this could be some long relationship. Their incredibly low price makes all this fun nearly free. Many owners of much finer rifles have found joy with the KL-3B as I have, it really is a good shooter!

Don't wait! They are a close-out, discontinued rifle. The supply WILL one day dry up.

JMHO,

ZVP

I pulled it apart and installed a cut down (to 29 coils) RWS 94 spring, honed the scored up chamber, removed the leather piston seal and made up an aluminum adaptor (screws in like the leather seal did) then snapped on an IZH -61 piston seal. It was a perfect fit. I then clipped off two coils from the trigger spring and lightly ground the trigger sear, then stoned it smooth with a Wa****a white stone and lightly molyed the sear surfaces.
The RWS 94 spring fits the factory spring guide perfectly, but the factory guide is too short, so I made a Delrin tophat with a 1.5" shank to more fully support the spring at the front end and control all vibration. I made the "brim"(flange) of the tophat 1/8th" thick. Works a treat! I'll chrony it tomorrow. RB

BesTunes@cs.com