Don’t oil your gun.

Don’t use or introduce any lubes into your compression chamber through the port or into the barrel. Also, do not use or introduce oils on the spring or into the cocking slot of the action. This lube migrates to the cylinder walls and weeps its way into the compression chamber.

The reason for this is that it causes detonation that damages the seal as well as causes the spring to fatigue and collapse and can actually cause the spring to fracture. It greatly increases the double recoil shock and that can damage your scope. It also causes your gun to have erratic velocity that seriously impacts the accuracy.

If properly tuned using the proper lubes, your gun can go for years without needing to be lubed internally although external linkage lubing and maintenance will need to be ongoing.

Charlie